## Slide 1
DEPARTMENT OF ELECTRONICS & COMMUNICATION
IoT Based
Smart Blind Stick
Assistive Technology for the Visually Impaired
Presented by: Student Name / Team
Guide: Prof. Guide Name
Academic Year 2024-25

## Slide 2
IoT Based Smart Blind Stick
2 / 10
Abstract
This project presents an IoT-based Smart Blind Stick built on the ESP32 DevKitC microcontroller, designed to assist visually impaired individuals in navigating safely and independently. The system integrates two HC-SR04 ultrasonic sensors (obstacle detection at front and pit/stair detection downward), a NEO-6M GPS module for live location tracking, a vibration motor and buzzer for multi-level haptic and audio alerts, and an SSD1306 OLED display for real-time status feedback.
The ESP32 connects to Wi-Fi and uploads GPS coordinates and obstacle distance data to a Supabase cloud database every 10 seconds, enabling remote monitoring by caregivers. Buzzer and vibration alerts are triggered with variable frequency patterns depending on obstacle proximity (close: 20 cm, medium: 50 cm, far: 100 cm). The downward sensor detects pits and stairs beyond 70 cm depth with a rapid double-pulse alert.
Programmed using Arduino IDE with C++ and key libraries (TinyGPS++, Adafruit SSD1306, HTTPClient), this low-cost and portable solution aims to significantly enhance the mobility, safety, and independence of visually impaired persons through IoT-driven assistive technology.

## Slide 3
IoT Based Smart Blind Stick
3 / 10
Objective
Obstacle Detection
Dual HC-SR04 ultrasonic sensors: one front-facing for obstacles, one downward-facing for pit/stair detection, with variable buzzer and vibration alerts.
GPS Tracking
NEO-6M GPS module decodes live coordinates via TinyGPS++ library and uploads to Supabase cloud every 10 seconds over Wi-Fi for caregiver remote monitoring.
Alert System
Provide audio (buzzer) and tactile (vibration) alerts for immediate feedback.
OLED Display
SSD1306 128x64 OLED (I2C on GPIO21/22) shows live OBS/DEP distances and active sensor state, giving the user visual system feedback.
Supabase Cloud
HTTP POST to Supabase REST API uploads GPS + obstacle data every 10s. Wi-Fi reconnection logic handles signal drops automatically.
ESP32 DevKitC
ESP32 DevKitC chosen for built-in Wi-Fi/BLE, dual-core CPU, multiple UART/I2C interfaces, and more GPIOs than Arduino Uno, all without extra modules.

## Slide 4
IoT Based Smart Blind Stick
4 / 10
Introduction
Global Context Over 2.2 billion people worldwide have visual impairment (WHO). Traditional white canes offer limited assistance and lack smart capabilities. Problem Statement Conventional sticks cannot detect elevated obstacles, open manholes, or wet surfaces. There is no location-sharing feature for caregiver monitoring. Our Solution A smart stick embedded with IoT sensors that detects obstacles, alerts the user, and shares GPS location providing safety and independence.
2.2B
Visually Impaired
Worldwide (WHO)
39M
Completely
Blind Persons
85%
Preventable with
Assistive Tech

## Slide 5
IoT Based Smart Blind Stick
5 / 10
Literature Survey
[1]
Soundarya RP et al., 2020 (IACIT)
Smart Blind Stick Using Arduino (REVA Univ.). Uses Arduino Mega 2560 + ultrasonic + IR sensors. Buzzer alerts at 30 cm. Trained users achieve 2x walking speed over untrained users.
[2]
Keerthana MM et al., 2024 (IJCRT)
IoT Enabled Smart Blind Stick (ATME Mysuru). ESP32-based system with 3 ultrasonic sensors (front/left/right), water sensor, APR voice module, and live GPS tracking via Android + Blynk app.
[3]
Mohd Khir et al., 2025 (MARI Journal)
SmartSight: IoT Smart Blind Stick with Weather Detection (UTHM Malaysia). Arduino + ESP8266 + GPS + GSM. Adds temperature/humidity sensor and water sensor. Avg user satisfaction 4.13/5.
[4]
Jyoth Singh et al., 2025 (IJCRT)
Smart Blind Aid Stick: Enhancing Mobility & Safety (SRK Institute). ESP8266 + ultrasonic + Blynk IoT app. Emergency SMS with GPS location on button press. Detects obstacles <20 cm.

## Slide 6
IoT Based Smart Blind Stick
6 / 10
Existing Model & Proposed System
Existing Model
Basic white cane - no electronics
No obstacle detection capability
No GPS or location tracking
Cannot detect elevated obstacles
No caregiver alert mechanism
No water / pit detection
VS
Proposed System
ESP32 DevKitC (38-pin) with built-in Wi-Fi
Dual HC-SR04: front obstacle + downward pit
NEO-6M GPS + Supabase cloud monitoring
Variable buzz patterns by obstacle proximity
SSD1306 OLED display for real-time status
Buzzer (GPIO23) + vibration motor (GPIO19)

## Slide 7
IoT Based Smart Blind Stick
7 / 10
Circuit Diagram
ESP32 DevKitC Pin Connections (from actual code)
ESP32
DevKitC (38-pin)
HC-SR04 #1
(Obstacle - Front)
TRIG=GPIO5 / ECHO=GPIO18
HC-SR04 #2 (Pit/Depth - Down)
TRIG=GPIO25 / ECHO=GPIO26
Buzzer (Active)
GPIO23
GPS Module
(NEO-6M)
TX=GPIO16 / RX=GPIO17 (UART2)
OLED Display
SSD1306 (128x64)
SDA=GPIO21 / SCL=GPIO22 (I2C)
Buzzer +
Vibration Motor
Vibration Motor: GPIO19
3.7V Li-ion
Rechargeable Battery

## Slide 8
IoT Based Smart Blind Stick
8 / 11
Source Code (Arduino / ESP32)
// ===== KEY DEFINITIONS =====
#define OBS_TRIG 5 // Obstacle sensor trigger
#define OBS_ECHO 18 // Obstacle sensor echo
#define DEP_TRIG 25 // Depth/pit sensor trigger
#define DEP_ECHO 26 // Depth/pit sensor echo
#define BUZZER 23 // Buzzer output pin
#define VIBRATION 19 // Vibration motor pin
// OLED on I2C: SDA=21, SCL=22
// GPS UART2: TX=16, RX=17
// ===== DISTANCE FUNCTION =====
float getDistance(int trig, int echo) {
digitalWrite(trig, HIGH);
delayMicroseconds(10);
digitalWrite(trig, LOW);
long dur = pulseIn(echo, HIGH, 30000);
return dur * 0.0343 / 2.0;
}
// ===== BUZZER ALERT LOGIC =====
if (depActive) { // Pit detected
buzz(100); delay(100); // Rapid double pulse
} else if (obs < OBS_CLOSE) { // <20cm
buzz(50); delay(50); // Very rapid pulse
} else if (obs < OBS_MEDIUM) { // <50cm
buzz(100); delay(150); // Medium pulse
} else if (obs < OBS_FAR) { // <100cm
buzz(100); delay(400); // Slow pulse
}
Libraries Used
WiFi.h | HTTPClient.h | Wire.h
Adafruit_GFX | Adafruit_SSD1306
TinyGPS++ (GPS decoding)
Supabase Cloud Upload (every 10s)
POST: latitude, longitude,
obstacle_distance (cm)
OLED Display Shows (Real-time)
OBS distance | DEP distance
Sensor status: OBS / DEP / OBS+DEP
Alert Thresholds (Obstacle Sensor)
CLOSE: <20 cm | MEDIUM: <50 cm
FAR: <100 cm | PIT DEPTH: >70 cm

## Slide 9
IoT Based Smart Blind Stick
8 / 10
Result & Discussion
2+1
Sensors
Accuracy
100cm
Obstacle Alert
FAR Threshold
10s
Cloud Upload
Interval
70cm
Pit Detect
Accuracy
Sensor Performance
Two HC-SR04 sensors reliably detected obstacles at CLOSE (<20 cm), MEDIUM (<50 cm) and FAR (<100 cm) with variable alert patterns. Downward sensor correctly triggers pit alert when depth exceeds 70 cm.
GPS Tracking
NEO-6M GPS decoded via TinyGPS++ on UART2 (GPIO16/17). Coordinates uploaded to Supabase REST API every 10 seconds. Wi-Fi auto-reconnect handles dropouts without system restart.
OLED Display
OLED shows live OBS/DEP readings, sensor status (OBS ACTIVE / DEP ACTIVE / OBS+DEP ACTIVE / NO DETECTION) and WiFi IP at startup. Updates every loop iteration.
Cloud Monitoring
Supabase cloud database receives JSON payload {latitude, longitude, obstacle_distance} every 10 s, enabling any caregiver with dashboard access to monitor the user in real time.

## Slide 10
IoT Based Smart Blind Stick
9 / 10
Conclusion
The IoT Based Smart Blind Stick successfully demonstrates an affordable and effective assistive technology for the visually impaired. By integrating ultrasonic sensors, IR sensors, GPS, GSM, and a water detection module with a microcontroller, the system provides real-time obstacle detection, ground hazard alerts, and continuous location monitoring for caregivers.
Field testing confirmed high accuracy in obstacle detection and reliable GPS tracking. The system is portable, lightweight, and operates for 8-10 hours on a single charge making it practical for daily use.
Future Scope
AI-based object recognition | Voice navigation assistant | Mobile app integration | Fall detection sensor | Solar charging module

## Slide 11
IoT Based Smart Blind Stick
10 / 10
References
1
Soundarya RP, Pooja Reddy B, Akshitha A, Anusha R, "Smart Blind Stick Using Arduino," International Journal of Advanced Research in Computer Science (IJARCS), Vol 11, Special Issue I, IACIT-2020, REVA University, Bengaluru, India, May 2020.
2
Keerthana MM, Madhusudhan S, Mahadev Prasad PS, Manu M, Vineeth Shandilya MJ, "IoT Enabled Smart Blind Stick," International Journal of Creative Research Thoughts (IJCRT), Vol. 12, Issue 5, ISSN: 2320-2882, ATME College of Engineering, Mysuru, May 2024.
3
Ainul Bahriah Mohd Khir, Nur Farah Aina Ahmad Mazrullah, Nurul Izzah Zahirah Che Kamarudin, Mazniha Berahim, "SmartSight: IoT-Based Smart Blind Stick with Weather Detection and Anti-Lost Function," MARI (Multidisciplinary Applied Research and Innovation), Vol. 6 No. 2, pp. 162-171, UTHM Malaysia, Feb 2025.
4
RP. Jyoth Singh, P. Jahnavi, T. Lavanya, M. Krishna Reddy, K. Tejaswini, "Smart Blind Aid Stick: Enhancing Mobility & Safety," International Journal of Creative Research Thoughts (IJCRT), Vol. 13, Issue 4, ISSN: 2320-2882, SRK Institute of Technology, Andhra Pradesh, April 2025.
5
Omkar Rajendra Solankar, Vikram Ramesh Thorat, Pratiksha Anil Shinde, Saniya Husen Shikh, "The Smart Blind Stick," Journal of Emerging Trends and Novel Research (JETNR), Vol. 4, Issue 3, ISSN: 2984-9276, Vidya Pratishthan’s Polytechnic College, Indapur, March 2026.
6
Espressif Systems, "ESP32 Technical Reference Manual," [Online]. Available: https://www.espressif.com. TinyGPS++ Library: https://github.com/mikalhart/TinyGPSPlus. Supabase Documentation: https://supabase.com/docs. Adafruit SSD1306 Library: https://github.com/adafruit/Adafruit_SSD1306